## Slide 1
1.)
CHAPTER 27:
Current and Resistance
serious
electric car:

## Slide 2
To measure the pressure difference, you need a meter across the pump.
2.)
Consider a pipe system through which water flows. What characteristics might that system have?
The Analogy
--It needs a pumping system that produces a pressure difference that will motivate water to flow.
--There is water flow. To measure the amount of flow that passes by per unit time, you need a meter located in the flow.
--There is resistance to flow created by the geometry of the pipe.
--So consider the points a, b and c shown in the upper section. Where is the flow rate the greatest?
Flow rate measures how much water passes by per unit time. It HAS to be the same at every point (otherwise, what happened to the water that didn’t make it?)

## Slide 3
--To measure the voltage difference across the battery, you need a voltmeter across the power supply.
3.)
Analogously, the lowly electrical circuit:
Simple Electrical Circuit
--A battery provides power by producing a voltage difference across its terminals. The voltage difference creates an electric field through the wires which motivates charge to move.
where coulombs/second is given a special name, the ampere (or amp).
--Current is defined as the amount of charge that passes by a point per unit time. Mathematically, this is:
--Current is measured with an ammeter placed directly into the circuit.

## Slide 4
4.)
--Oddly, when analyzing circuits, current is defined as the motion of POSITIVE CHARGE CARRIERS. That means that “current” (called conventional current to separate it from what is called electron current, which highlights what’s actually happening with electron flow in a circuit), flows from higher to lower voltage. Weird, but that’s the convention.
--A resistor is a circuit element that does two things:
a.) Resistors limit the current in the sense that a large resistance means relatively small current, and a small resistance means relatively big current.
b.) Resistors dissipate energy in the sense that they convert electrical energy into other forms of energy (heat, light, etc.).
Note: Because current is a measure stuff (charge) passing by per unit time, the current entering a resistor must equal the current exiting a resistor. Just sayin ...

## Slide 5
Ohm’s Law
5.)
--It has been observed that the voltage across a resistor is proportional to the current through the resistor, or:
--The proportionality constant that makes that relationship into an equality is called the resistance R of the resistor, and the relationship becomes:
--As R=V/i, the unit for resistance is the volts/amps, or ohms. The symbol for ohms is (i.e., a capital omega).
--This is called Ohm’s Law.
--Resistors are temperature dependent. We don’t do anything with this.
--Note that the resistance of a wire of length L, cross sectional area A and resistivity is:

## Slide 6
Lab Cover Artwork
6.)
--You are now in a position to come up with some great lab cover artwork. To wit:
http://home.earthlink.net/~cfletcher
mobile ohm
ohm run
ohm plate
ohm on the range
Or go to:

## Slide 7
Secret Resistor Code (courtesy of Mr. White)
7.)

## Slide 8
Resistor Color Code
foruth band
(d)
third band
(c)
second band
(b)
first band
(a)
The bands are colored with each color denoting a number.
black 0 green 5
brown 1 blue 6
red 2 violet 7
orange 3 gray 8
yellow 4 white 9
last band gold 5%
last band silver 10%
last band blank 20%
The bands decode as:
Example: If the resistor’s value is , the bands would be colored:
first band: green (for 5);
second band: red (for 2);
third band: blue (for 6);
fourth band: silver (to show
a tolerance of 10%)
8.)

## Slide 9: Example 1: (courtesy of Mr. White)
Note 2. DC voltage (short for direct current voltage) sets up an electric field that is always in the same direction. AC voltage (alternating current voltage) sets up an electric field that alternates in direction. An AC voltage source will produce some amount of power. The DC source that provides the same amount of power is called AC source’s RMS voltage. It is used in exactly the same way as a DC voltage.
The video projector here uses a 120Vrms potential, and “draws” 2.7 Amps of current
a.) What is its resistance?
Note 1: When it comes to power supplies, the electrical potential difference across the power supply’s terminals is often referred to as the power supply’s potential.
So using Ohm’s Law:
9.)

## Slide 10
The video projector here uses a 120Vrms potential, and “draws” 2.7 Amps of current
b.) What would be the current if the voltage used to run the machine was only 12 volts?
10.)

## Slide 11: Example 2: (courtesy of Mr. White)
You have an LED with essentially no resistance, that takes 300 mA of current to light. You have a 9 Volt battery that you’d like to use to light the LED.
a.) What will your circuit look like?
b.) How large a resistor should you use to make sure that the LED doesn’t blow out?
c.) What color code should you look for on your resistor?
orange, black, black, blank
11.)

## Slide 12: Example 3: Current passes through a resistor? During some period of time, assume q’s worth of charge passes through the resistor. How much work is done on that charge?
Assume the voltage on either side of the resistor is and respectively. With that, we can write:
12.)
Example 4: How much power is being dissipated by the resistor in the previous problem?
Power is work per unit time, so:
In short:
This is generally true, but according to Ohm’s Law, we an write:

## Slide 13: The most general expression for the power rating of an element is:
Power
13.)
where i is the current through the element and V is the voltage across the element. Its unit is WATTS.
When dealing specifically with a resistor, where Ohm’s Law holds sway, the relationship can be written as:
This is the relationship you would use if you wanted to determine how much power a power supply was providing to a circuit.
or on very rare occasions,

## Slide 14: Example 5: A light bulb is rated at 120 volts (RMS), 75 W. Assuming the bulb is powered by a 120 V RMS power supply, determine:
14.)
a.) the current in the bulb?
b.) the resistance of the bulb?

## Slide 15: Example 6: An electric heater draws 15 amps on 120 volts (RMS). It operates 3 hours/day for 30 days/month. PG&E charges $.08 per kilowatt-hour.
15.)
a.) how much power does the heater draw?
b.) how much does it cost to run the heater for a month?
A kilowatt is a thousand watts, which is a thousand joules per second. A kilowatt-hour is a thousand joules per second times an hour (3600 seconds), which is a unit of energy (that’s what the power company is charging you for when it registers your kW-hr usage for the month, the energy you use). We can leave things in kW-hrs, though, and just use dimensional analysis on this: